## Slide 1: Electrical Power System Concept of Operations Shipboard Power System Fundamentals Revision of 7 February 2026
Dr. Norbert Doerry
http://doerry.org/norbert/MarineElectricalPowerSystems/index.htm
© 2026 by Norbert Doerry This work is licensed via: CC BY 4.0 (https://creativecommons.org/)

## Slide 2: Essential Questions
What is an electrical power system concept of operations? | Remember
What is an electrical power system concept of operations used for? | Understand
How is an electrical power system concept of operations developed? | Apply

## Slide 3: Introduction
The electrical power system concept of operations (EPS-CONOPS) documents how the designer intends for the ship’s electrical power system is to be:
  Designed
  Operated during normal, nominal operations
  Operated during restorative operations
  Maintained
  Repaired
  Upgraded
EPS-CONOPS is a working document
  Content is generated during the design process as needed to support design and analysis
  Serves as single source of truth to ensure consistency for calculations, analyses, and simulations
IEEE Std 45.3 provides guidance for EPS-CONOPS content

## Slide 4: EPS-CONOPS uses
Serve as a single source of truth for design assumptions needed to support design and analysis activities (including simulations).
Define standard electric plant line-ups.
Reflect knowledge gained from electrical power system studies.
Provide the basis for establishing load factors and load models in the electric power load analysis (EPLA).
Provide operators, designers, and maintainers with insight as to how the designers intended for the electrical power system to operate under different conditions.

## Slide 5: EPS-CONOPS as part of the design process
Part of the digital thread within a digital design environment.
  Evolution of the EPS-CONOPS should be traceable over time.
  May refer to other configuration managed documents or databases that serve as a single source of truth.
    EPS-CONPS should only link to authoritative sources of data.
As the EPS-CONOPS evolves, changes should be examined to determine if analyses should be repeated to reflect the changes.

## Slide 6: EPS-CONOPS content
Overarching assumptions and requirements
Operating conditions
Operational scenarios
Mission / payload system information
Electric load Information
Electrical power system machinery lineups
Nominal operations
Restorative operations
Electrical power system / ship system trade studies
Maintenance / repair strategy
Modernization strategy

## Slide 7: Overarching assumptions and requirements
Typical overarching assumptions and requirements documented in the EPS-CONOPS:
  Margin and service life allowance policy
  Ship service life
  Redundancy requirements
  Survivability requirements
  Minimum and maximum loading on generator sets under normal conditions
  Functions of energy storage
  Identification of all separately derived systems
  QOS t1, t2 and Mean Time Between Service Interruption (MTBSI) for each separately derived system
  Power quality interface standards for each separately derived system
  Grounding system type for each separately derived system
  Identification of converters as isolated or non-isolated

## Slide 8: Operating Conditions
Typical operating conditions include
  Cruise
  One or more Missions (or functional)
  Shore
  Anchor
  Emergency
Should include guidance for determining which mission system equipment and support system equipment are online
  Particularly important to identify if large loads are online
Used in
  Electric Power Load Analysis (EPLA)
  Endurance fuel calculations
  Annual fuel calculations

## Slide 9: Operational scenarios
Operational scenarios consist of a timeline of
  Operating conditions
  Use of large loads
  Use of significant smaller loads
  Associated speed time profiles
Used in
  Annual fuel calculations
  Energy storage system power and energy capacity sizing

## Slide 10: Mission / payload system information
Load models for large loads and smaller but significant loads
  Detail power consumption under different operating modes of the equipment.
  Identify percentage of time in each operating mode in each operational condition.
Creation of load models
  Initially by analogy with similar ships.
  Refined as knowledge is gained on how the ship is intended to be operated.
Used in
  Creation of load factors for EPLA.

## Slide 11: Electric load information
Special considerations for specific loads
  Impact on electrical power system lineups.
  Loads that may not meet power interface requirements.
Special considerations for the power system
  Features in the power system, or power system operations, to mitigate loads not meeting power system interface requirements.
  Conditions where the power system may not meet power system interface requirements.
Used in
  Design of the power system.

## Slide 12: Electrical power system machinery lineups
For each operating condition
  Preferred electric plant line-up
    Bus tie breaker position
  Generator set scheduling table
  Energy storage system mode of operation
Used in
  EPLA – including energy storage system sizing
  Endurance fuel calculations
  Annual fuel calculations

## Slide 13: Nominal operations
Describe how the electric plant is intended to operate:
  For each of the operating conditions, what performance attributes should be optimized.
  The process for transitioning between operating conditions; what is the order of changes to the electric plant lineup.
  The method employed for power management; what is the process for bringing additional generation capacity online and dropping offline excess generation capacity?
  The degree of autonomy expected of electrical power system controls for each operating condition.
Used in:
  Creating simulation models for dynamic simulations.

## Slide 14: Restorative operations
Describe how the electric plant is intended to be restored to nominal operation following failure or damage
  Load shedding strategy and implementation.
  Casualty power strategy and implementation. (if a casualty power system is installed)
  Dark ship start procedures. (no generation online, but energy storage systems functional)
  Dead ship start procedures. (no generation online; all energy storage systems depleted)
  Zonal survivability assumptions and procedures.
  Compartment survivability assumptions and procedures.
Used in
  Creating simulation models for dynamic simulations.
  Survivability analyses.
  Quality of Service and Reliability analyses.

## Slide 15: Electrical power system / ship system trade studies
Document insights gained from analyses and trade-studies.
Used in
  Ensuring all other analyses and design activities reflect the insights.

## Slide 16: Maintenance / repair strategy
Document maintenance and repair strategies of electrical equipment.
Used in:
  Determining how much redundancy to provide.
  Determining frequency of service interruptions for QOS analysis.
  Determining Mean-Time to Repair for reliability analysis.
    Determining how many spare parts are required onboard.

## Slide 17: Modernization strategy
Describe features in the power system design that facilitate modernization:
  How service life allowance should be allocated to the various load centers.
  The number and rating of spare breakers in each switchboard and load center.
  Load equipment for which space, weight, power, and cooling has been allocated, but the equipment is not intended to be installed until a time after ship delivery.
  Power system equipment for which extra capacity is enabled but not provided at ship delivery. Examples include slots for additional power converter modules in a converter, or the ability to replace a generator set with one of higher rating without having to modify switchboards or other distribution system equipment.
  List of power system equipment that is expected to be replaced during the ship’s service life. Specify whether an equipment removal route, bolted equipment removal plate (BERP) or welded equipment removal plate (WERP) should be considered or installed onboard ship.
Used in
  Design of the power system.
  General arrangements.

## Slide 18: EPS-CONOPS development
Should be developed incrementally in a configuration managed environment.
Content should be developed in the order required to support ongoing analyses.
  Information needed to support the Electric Power Load Analysis (EPLA) and endurance fuel calculations typically required first.
  The creation of some content may be delayed to preliminary design.