## Slide 1: Propulsion System Concept of Operations Shipboard Power System Fundamentals Revision of 7 February 2026
Dr. Norbert Doerry
http://doerry.org/norbert/MarineElectricalPowerSystems/index.htm
© 2026 by Norbert Doerry This work is licensed via: CC BY 4.0 (https://creativecommons.org/)

## Slide 2: Essential Questions
What is a Propulsion System Concept of Operations? | Remember
What is a Propulsion System Concept of Operations? | Understand
How is a Propulsion system concept of operations developed? | Apply

## Slide 3: Introduction
The propulsion system concept of operations (PS-CONOPS) documents how the designer intends for the ship’s propulsion system is to be:
  Designed
  Operated during normal, nominal operations
  Operated during restorative operations
  Maintained
  Repaired
  Upgraded
PS-CONOPS is a working document
  Content is generated during the design process as needed to support design and analysis
  Serves as single source of truth to ensure consistency for calculations, analyses, and simulations

## Slide 4: PS-CONOPS uses
Serve as a single source of truth for design assumptions needed to support design and analysis activities (including simulations).
Define standard propulsion system line-ups.
Reflect knowledge gained from propulsion system studies.
Provide operators, designers, and maintainers with insight as to how the designers intended for the propulsion system to operate under different conditions.

## Slide 5: PS-CONOPS as part of the design process
Part of the digital thread within a digital design environment.
  Evolution of the PS-CONOPS should be traceable over time.
  May refer to other configuration managed documents or databases that serve as a single source of truth.
    PS-CONOPS should only link to authoritative sources of data.
As the PS-CONOPS evolves, changes should be examined to determine if analyses should be repeated to reflect the changes.

## Slide 6: PS-CONOPS content
Overarching assumptions and requirements
Propulsion system machinery line-ups
Nominal Operations
Restorative Operations
Propulsion system trade studies
Maintenance / repair strategy
Modernization strategy

## Slide 7: Overarching assumptions and requirements
Typical overarching assumptions and requirements documented or referenced in the PS-CONOPS:
  Margin and service life allowance policy
  Ship service life
  Redundancy requirements
  Survivability requirements
  Maneuvering requirements
  Turning requirements
  Crash stop / reversal requirements
  Dynamic positioning requirements
  Autopilot requirements
  Propulsion system lineups for endurance calculations

## Slide 8: Propulsion system machinery lineups
For each operating condition detailed in the EPS-CONOPS
  Propulsion scheduling table
  Propulsion system configurations
Used in
  Endurance fuel calculations
  Annual fuel calculations

## Slide 9: Nominal operations
Describe how the propulsion system is intended to operate:
  For each of the operating conditions, what performance attributes should be optimized.
  The process for transitioning between propulsion system lineups.
  Limitations for the use of auxiliary propulsion motors and thrusters.
  Expected control modes (constant power, constant torque, or constant speed) and limitations on the use of control modes.
  Limitations, if any, on operating in trail-shaft.
  Uses of jacking gear and turning gear.
  Shaft grounding system / cathodic protection system description.
  Operation of steering gear.
Used in:
  Creating simulation models for dynamic simulations.

## Slide 10: Restorative operations
Describe how the propulsion system is intended to be restored to nominal operation following failure or damage
  Local control modes.
  Use of clutches, shaft brakes, shaft seals, etc. in restorative operations.
  Limitations on ship speed for different types of casualties and restorative methods.
  Emergency steering procedures.
Used in:
  Creating simulation models for dynamic simulations.
  Survivability analyses.
  Reliability analyses.

## Slide 11: Propulsion system trade studies
Document insights gained from analyses and trade-studies.
Used in:
  Ensuring all other analyses and design activities reflect the insights.

## Slide 12: Maintenance / repair strategy
Document maintenance and repair strategies of propulsion system equipment.
Used in:
  Determining how much redundancy to provide.
  Determining Mean-Time to Repair for reliability analysis.
  Determining how many spare parts are required onboard.

## Slide 13: Modernization Strategy
Document features, if any, within the propulsion system design that facilitate modernization of the ship.
Used in:
  Design of the propulsion system.
  General arrangements.

## Slide 14: PS-CONOPS development
Should be developed incrementally in a configuration managed environment.
Content should be developed in the order required to support ongoing analyses.
  Information needed to support endurance fuel calculations and annual fuel calculations typically required first.
  The creation of some content may be delayed to preliminary design.