## Slide 1: Shipboard Power System as a Microgrid Shipboard Power System Fundamentals Revision of 20 December 2025
Dr. Norbert Doerry
http://doerry.org/norbert/MarineElectricalPowerSystems/index.htm
© 2025 by Norbert Doerry This work is licensed via: CC BY 4.0 (https://creativecommons.org/)

## Slide 2: Essential Questions
What is a microgrid? | Remember
What are the implications of a limited inertia system? | Understand
What are the implications of a limited generation capacity? | Understand
What are the implications of interconnecting with the terrestrial power system? | Understand

## Slide 3: Microgrid Definition
IEEE Std 2030.7 defines a microgrid as:
  “A group of interconnected loads and distributed energy resources with clearly defined electrical boundaries that acts as a single controllable entity with respect to the grid and can connect and disconnect from the grid to enable it to operate in both grid-connected or island modes.”
Distributed energy resources (DER) are further defined as:
  “Sources and groups of sources of electric power that are not directly connected to the bulk power system; they include both generators and energy storage technologies capable of exporting power.”
Modes
  When a microgrid is electrically connected to the grid it is in the “Steady state connected” mode.
  When a microgrid is operating disconnected from the grid it is in the “Steady state islanded” mode.
  Transition modes include “Unplanned islanding”, “Planned islanding”, “Black start”, and “Reconnect.”

## Slide 4: Shipboard power systems as a microgrid
Not a perfect fit
  Not all ships can connect to the grid.
  Some ships can connect to the grid and receive power from the grid, but cannot operate generator sets in parallel with the grid.
  Even ships that can operate generator sets in parallel with the grid typically only do so for short periods of time.
Ships at sea are equivalent to a microgrid operating in “steady state islanded” mode.
DERs onboard ship are typically gas turbine generator sets or diesel generator sets

## Slide 5: Limited inertia systems
Within the context of a power system, inertia is …
  The amount of stored energy that can be rapidly applied to maintain voltage and frequency due to transients from changing loads
Sources of inertia
  Generator sets
    Rotational mechanical inertia of the rotor
  Power electronic converters
    Stored electrical energy in dc link capacitance
Terrestrial Grid is considered an infinite bus with infinite inertia
  Changes in loads result in only local transient responses
Microgrids and shipboard power systems in islanded mode have limited inertia.
  Changes in load results in system voltage and frequency transients.
  Can lead to power quality issues or even generator sets dropping offline if not controlled properly.

## Slide 6: Limited Generation Capacity
Terrestrial Power Systems
  Real Power is scheduled
  Reactive Power is a function of network topology
Islanded microgrids and shipboard power systems
  Requires active control methods to balance supply and consumption of real and reactive power when generator sets are paralleled.
    Real Power is shared via either frequency droop or control signals (either analog or digital)
    Reactive power is shared via either voltage droop or control signals (either analog or digital)
  Energy storage may be employed to augment generation when needed.
  Load management may be employed if online generation capacity is less than the online load.
    Typically implemented as load shedding

## Slide 7: Interconnecting with the Terrestrial Grid
Terrestrial microgrids
  DER operation and grid operation are integrated when in the steady state connected mode.
Shipboard power systems
  Rarely operate for extended periods of time with shipboard generator sets paralleled with the terrestrial grid.
  Many ships will “break before make” such that the transfer to shore-power does not involve the paralleling of generator sets with the grid.
  Those ships that can operate paralleled to the grid usually only do so during the transfer of load to and from shore-power. (make before break)