## Slide 1: Propulsion Motor Shipboard Power System Fundamentals Revision of 1 February 2026
Dr. Norbert Doerry
http://doerry.org/norbert/MarineElectricalPowerSystems/index.htm
© 2026 by Norbert Doerry This work is licensed via: CC BY 4.0 (https://creativecommons.org/)

## Slide 2: Essential Questions
What components comprise a Propulsion Motor subsystem? | Remember
What is the impact of operational profiles on propulsion motor subsystem design? | Understand
What are the control modes for a propulsion motor and when should each be used? | Understand
What are the sources of losses in a propulsion motor and how are they calculated? | Apply

## Slide 3: Components of a propulsion motor subsystem
Propulsion Motor
Motor Drive
Propulsion Transformer
Electrical Filters
Dynamic Braking Resistor
Shaft Bearings
Thrust Bearing
Cooling System
Monitoring and Control System
Shaft Grounding System
Cables

## Slide 4: Propulsion Motors
Synchronous Motors
  Most common
  Rotating field coil powered by exciter
  Shaft speed proportional to frequency of power provided to it.
Permanent Magnet Motors
  Synchronous motor with field coil replaced by permanent magnet
  More power dense and efficient than synchronous motor
  Usually more expense than synchronous motor
Induction Motors
  Current induced into field coil
  Rugged and robust, but less power dense and efficient than synchronous motor
  May be less expensive than synchronous motor
Direct Current Motors (brushed commutator)
  Once very common, seldom used in new designs
  Brushes limit operating voltage to 1 kV
  High maintenance costs associated with brushes
Superconducting Motors
  Synchronous motors with either or both the field winding and/or stator winding made of superconducting wires.
  Can be very power dense and more efficient than synchronous motors
  High cost
Homopolar Motors
  Direct Current machines without commutator
  Low voltage – high current machines
  Very power dense and efficient
  High cost

## Slide 5: Motor Drive
Converts power of the type provided by the electrical distribution system (or propulsion transformer) to the type needed by the motor.
Also controls the dynamic braking resistor when performing a crash back maneuver.
DC Link Converter.
  Front end stage converts the input power to dc (voltage or current)
    Passive (diode rectifier) – high harmonic currents
    Active (power electronics) – better control of current waveform properties
  Inverter stage converts the dc to the type needed by the motor
Cycloconverter.
  Directly converts ac of one frequency to ac of a lower frequency
    Lower frequency may result in larger propulsion motor
  High harmonic currents at interface with power system

## Slide 6: Propulsion Transformer
Usually converts three phase power from the electrical distribution system to six or more phases for use by the motor drive.
  More phases can reduce harmonic currents at interface with the electrical distribution system.
Can also produce power at the voltage needed by the motor drive.
Reduces common mode currents entering or leaving the connection to the electrical power distribution system.
May be omitted if the motor drive and electrical power system interfaces are compatible.

## Slide 7: Electrical Filters
Used to reduce non-fundamental frequency components of the currents at the interface with the electrical power distribution system.
  Goal is to achieve interface standards
Can address both “differential mode” and “common mode” currents.
Can be either passive (no power electronics) or active (with power electronics).

## Slide 8: Dynamic Braking Resistors
Used to dissipate regenerative power in motor drives that are not able to provide the power back onto the power system.
The regenerative power is extracted from the rotational energy of the shaft (not the ship) during a crash-back maneuver.

## Slide 9: Shaft and Thrust Bearings
Shaft bearings
  Support the shaft.
  Ensure proper shaft alignment.
  May be integrated into motor housing.
Thrust bearing
  Transfer longitudinal thrust from the propeller shaft to the ship’s hull and structure.
  May be located on either end of the motor.

## Slide 10: Cooling System
High power components may require cooling
  Motor
  Motor drive
  Dynamic braking resistor
  Electrical Filter
May have multiple “loops”
  Air
  Glycol-water mixtures
  Fresh water
  Sea water (intake and discharge overboard)

## Slide 11: Monitoring and Control System
Functions:
  Coordinate embedded controllers.
  Monitor sensors.
  Interact with overall ship-wide machinery control system.
  Implement control modes.
  Establish set-points for the embedded controllers.
May be …
  Integrated with the motor drive controller.
  Stand alone.

## Slide 12: Control modes
Constant Power
  Normal conditions when precise speed control not required.
  Appropriate for use in heavy seas.
  Reduces impact on prime mover.
Constant Speed
  Used when precise speed control needed.
  Appropriate for underway replenishment.
Constant Torque
  Used when constant power could result in over torquing the shaft.
  Appropriate for use in very high sea states, debris laden water, and ice laden water.
Coast Guard Cutter Polar Star (WAGB 10) transits through pack ice (USCG Photo)

## Slide 13: Shaft Grounding System
Used to limit galvanic corrosion of the shaft and propeller.
Shaft grounding system often employ a metallic brush on the shaft that is electrically connected to the hull of the ship.
Shafts may include an insulating coupling to prevent the flow of shaft currents.

## Slide 14: Cables
Interconnect electrical interfaces of equipment.
Incorporate design features to …
  Mitigate the impact of common-mode currents.
  Control the electric field within insulation to maximize insulation life.

## Slide 15: Sources of losses
Motors, Motor Drives, Propulsion Transformers
  No load losses.
  Losses proportional to current squared.
  Losses may be reduced by using multiple motors and motor drives on the same shaft – use only one motor and drive at low power levels.
Electrical Filters
  No load losses.
  Losses proportional to non-fundamental frequency current components squared.
Shaft Bearings and Thrust Bearings
  Very low losses.
Cooling Systems
  Power consumed by the cooling system is usually considered a loss.
  Losses can be considerable at low power levels.

## Slide 16: Operational Profiles
Objective: minimize losses at ship speeds that the ship operates for long periods of time.
If operate most of time at high speed, then high full-power efficiency is beneficial.
If operate most of time at low speed, then part-load efficiency is very important.
  Multiple motors and motor drives per shaft.
  Motors with better part load efficiency.