## Slide 1: Control interaction with mission systems Shipboard Power System Fundamentals Revision of 6 February 2026
Dr. Norbert Doerry
http://doerry.org/norbert/MarineElectricalPowerSystems/index.htm
© 2026 by Norbert Doerry This work is licensed via: CC BY 4.0 (https://creativecommons.org/)

## Slide 2: Essential Questions
When should mission systems and the power systems controls communicate? | Understand
What are examples of mission system - power system communication? | Remember
How are mission system – power system control interfaces implemented? | Understand
What are potential design issues with respect to mission system – power system communications? | Understand

## Slide 3: Reserve Power
Shipboard power systems are designed to supply the operating load at all times.
Reserve power is online generation capacity and energy storage capacity in excess of the operating load that may be used for powering additional loads.
To minimize fuel consumption, a ship may operate with less reserve power then needed to cover every contingency for additional loads.
  Control interaction between the mission systems and the power system controls enable the power system to have sufficient online generation capacity to serve the operating loads
    May require loads to delay increasing their power consumption.
    May require the power system to shed long-term interrupt loads while additional generation capacity is brought online.

## Slide 4: Examples
Large Load
  When operating at maximum power, a large load may require more than 20% of the online power capacity.
  Example: Propulsion motors.
    The maximum power used by a propulsion motor may be limited by the power system to prevent overloading the generator sets.
    If more propulsion power is needed, the propulsion motor requests additional power and the power system brings online additional generator sets (power system control may shed long term interrupt loads while additional generator sets are brought online). The propulsion motor may not use the additional power until given permission to do so by the power system controls.
  Example: Large exhaust fans on a mechanical drive roll-on-roll off (RORO) ship
    Fans must gain permission to start from the control system before starting.
Pulsed Load
  If unconstrained, the power and current waveforms of a pulsed load may be such that the power system cannot provide a voltage waveform within interface standards.
  Negotiations between the pulsed load and the power system may be employed so that the voltage waveforms are within interface standards while the pulsed load draws the negotiated power and current waveforms.
    Control mode of generator sets may change from fuel economy to responsiveness.
Load Shedding
  Commanding loads to enter a reduced power consumption state may be preferable to shutting off power to them completely; the recovery time could be considerably shorter.
  The load may have multiple power limit levels corresponding to different levels of capability.

## Slide 5: Implementation
The interface between the mission system equipment and power system controls should include definitions for all seven layers of the Open Systems Interconnection (OSI) Model.
  Physical Layer
  Data Link Layer
  Network Layer
  Transport Layer
  Session Layer
  Presentation Layer
  Application Layer
A simple command-response application layer protocol could be …
  Load request for use of power from power system
  Power system grants request or commands to stand by
  Load acknowledges power system response and behaves accordingly
    If load commanded to standby, power system grants request when the power system is ready
    Load acknowledges power system response
Behavior of the load and power system if the protocol is not completed within a specified time should be clearly defined.
Protocol should be described in the Interface Control Document (ICD).