## Slide 1: Cybersecurity Shipboard Power System Fundamentals Revision of 6 February 2026
Dr. Norbert Doerry
http://doerry.org/norbert/MarineElectricalPowerSystems/index.htm
© 2026 by Norbert Doerry This work is licensed via: CC BY 4.0 (https://creativecommons.org/)

## Slide 2: Essential Questions
What risk management processes for addressing shipboard machinery control cybersecurity are used? | Understand
How can cybersecurity be implemented in a shipboard power system? | Understand
How can cybersecurity implementations impact the operation of a shipboard power system? | Understand

## Slide 3: Cybersecurity - threats
Onboard ship
  Introduced during manufacturing at OEM
  Prior to installation onboard ship
  Malicious actors onboard ship
    Ship’s crews
    Maintenance personnel
    Visitors
    Other
  Inadvertent actors – usually careless members of ship’s crew.
Off the ship
  Cyberattacks

## Slide 4: Cybersecurity risk management
Risk Management
  Identify possible negative outcomes
  Tracing possible negative outcomes to causes
  Assessing the likelihood and impact of the possible negative outcomes
  Assigning a level of risk to the possible negative outcomes
  If level of risk is assessed high enough, develop and implement risk mitigation plans
Cybersecurity Resilience
  Framework for implementing cybersecurity risk management
  Procurement of applicable onboard systems and equipment should include requirements for cybersecurity resilience

## Slide 5: Elements of cybersecurity resilience
Identify
Protect
Detect
Respond
Recover
Govern
ABS
IACS UR E26
NIST
Cybersecurity
Framework 2.0

## Slide 6: Identify
Configuration management of computer-based systems
  Regularly inventory hardware and software
  Ensure other elements are applied to all computer-based systems
Periodic review of documentation describing roles and responsibilities of personnel in the management, operation, and governance of computer-based systems
  Ensure documentation is up to date and configuration managed
  Ensure personnel are aware of their roles and responsibilities

## Slide 7: Protect
Implement safeguards to limit or contain the impact of a cybersecurity incident
Group computer-based systems into security zones
  Stand-alone or connected to other security zones or networks through controlled data communication
  Security zones should align with ship’s zone boundaries where possible
  Controlled data communication implemented via …
    Firewalls
    Routers
    One-way data flow techniques
Avoid or mitigate the impact of denial-of-service (DoS) attacks
Employ antivirus, anti-malware, and antispam software
Use access controls (user and device authentication)

## Slide 8: Detect
Implement methods to recognize and identify inappropriate activity within a computer-based system
Verify that the computer-based system correctly implements security functions

## Slide 9: Respond
Minimize the impact of a cyber event on a computer-based system and associated networks
Prevent the cyber event from impacting other computer-based systems
Develop and configuration manage incident response plans
  Train personnel to respond to cyber events using the incident response plans
Techniques
  Redundant computer-based systems
  Local controls that serve as backup to primary control system (required for some computer-based systems by IMO)
  Stop network communication into or out of a security zone (computer-based systems within the zone should still be capable of functioning)
  Should be capable of putting a computer-based system into a safe state

## Slide 10: Incident Response Plan contents (IACS UR E26)
Breakpoints for the isolation of compromised systems
Description of alarms and indicators signaling detected ongoing cyber events or abnormal symptoms caused by cyber events
Description of expected major consequences related to cyber incidents
Response options, prioritizing those which do not rely on either shut down or transfer to independent or local control
Independent and local control information for operating independently from the system that failed due to the cyber incident

## Slide 11: Recover
If possible, restore all computer-based systems and associated networks to normal operation
Develop and configuration manage recovery plans
  Train personnel to respond to cyber events using the recovery plans
  Base recovery plans on recovery objectives (IACS UR E26)
    System recovery: methods and procedures to recover communication capabilities shall be specified in terms of Recovery Time Objective (RTO). This is defined as the time required to recover the required communication links and processing capabilities.
    Data recovery: Recovery Point Objectives (RPO) should specify methods and procedures to recover data necessary to restore safe state of the hardware, software and networks that monitor and control onboard systems and to restore safe ship operation. The longest period of time for which an absence of data can be tolerated should be specified.

## Slide 12: Recovery plan contents (IACS UR E26)
Instructions and procedures for restoring the failed system without disrupting the operation from the redundant, independent or local operation.
Processes and procedures for the backup and secure storage of information.
Complete and up-to-date logical network diagram.
The list of personnel responsible for restoring the failed system.
Communication procedure and list of personnel to contact for external technical support including system support vendors, network administrators, etc.
Current configuration information for all components.

## Slide 13: Cybersecurity operational impact
Cybersecurity is not passive
  Crew training is critical
  Documentation supporting cybersecurity resilience should be regularly reviewed and updated
  Regular exercises should be carried out on detecting, responding, and recovering from cyber incidents
Cybersecurity requires an investment in crew time and resources
  Payoff is fast recovery in response to a cyber incident
  Lost operational time can be very expensive